## Slide 1: Networking for DevOps
Or
(How I learned to stop worrying and love subnet masks)

## Slide 2: A brief history (hello?)
Once upon a time two hosts, Harry and Sally, saw each other across a crowded room. But they could not speak
So we added coax cabling between them, a network interface card (NIC) on each host and some basic voltage encoding:
  +5V is binary 1, -5V is binary 0
The voltage has to persist across the whole wire to send the message
EVERY machine gets EVERY sent message (the same COLLISION DOMAIN)
And all was well.
Harry
Sally
01101110
Message

## Slide 3: A brief history (who dis?)
Then Frank turned up and started talking on their wire. Confusing!
So we gave each host NIC a MAC ADDRESS and added a HEADER to the MESSAGE stating where each message is from (SOURCE) and where it is going (DESTINATION)
The message and it’s header together are called a FRAME
This approach is called “shared bus” topology.
And all was well…
Until Sally’s wire gets unplugged and the whole network goes down because the electrical signal is lost.
Harry
Sally
Frank
Message
Header
Frank ->
-> Sally

## Slide 4: Bytes, bits, and MAC
A bit is binary – can be 1 or 0
8 bits make a byte
MAC Addresses are 48 bit (6 byte) hexadecimal conversions of the binary address of the NIC
MAC Addresses are set during NIC manufacture and are globally unique
byte

## Slide 5: Layers
7 - Application
6 - Presentation
5 - Session
4 - Transport
3 - Network
2 – Data Link
1 - Physical
Theoretical OSI Model
Application
Transport
Network/Internet
Network Interface
TCP/IP
(The bit that matters)
2
3
4
7
HTTP, SSH, L7 Firewall
TCP, UDP, L4 Firewalls
IP, Routers
NIC, Switch, MAC
Hardware, Copper, Fibre

## Slide 6: Packets and Frames
A FRAME is the Message (sometimes called a payload), The Source MAC address and the Destination MAC address bundled together.
Frames are used for local traffic and only at Layer 2 – NIC – Data Link
Frames only know “next hop”
A PACKET inserts additional HEADER information at Layer 3 when the message is being transmitted outside of the local network
Packets know the original source and the final destination
Layer 4
Layer 3
Layer 2
Layer 7
Dest MAC
Source MAC
Message
Layer 4
Layer 2
Layer 7
Dest MAC
Source MAC
Message
Protocol
Protocol
Source IP
Destination IP

## Slide 7: A brief history (hub-alicious)
So we added a HUB with each host connected in a star pattern to a single electrical bus.
Everybody still gets everything sent (still same COLLISION DOMAIN)
And all was well again…
Until two messages are sent together (collision) and we have to wait for the line to clear and retransmit. Slooooooow.
Harry
Sally
Frank
HUB
Message
Header

## Slide 8: A brief history (switching up)
So Philips invented the SWITCH that had an electrical bus for every Ethernet port.
Which meant a separate collision domain for every Ethernet port.
The switch queues messages so no more retransmitting.
Even better – switches intelligently send messages to the correct destination Ethernet port
It does this by building an ARP table using ONLY the Layer 2 frame header
Hosts only receive the messages meant for them
And all was pretty swell.
Harry
Sally
Frank
SWITCH
Message
Header
Ethernet:
Often shortened to:
eth (e.g. eth0)
Or just:
e (e.g. (e0)
At the OS level

## Slide 9: ARPing about
ARP table = Address Resolution Protocol
If the switch receives a message and doesn’t already know the address of the destination device it sends a BROADCAST packet to the BROADCAST DOMAIN.
The broadcast domain IP is the last IP address in the subnet range
The responding device has it’s MAC address added into the ARP table on the switch
Future packets can then be sent straight to that device without the broadcast request
Harry | D3:45:C1:98:22:A4
Sally | F5:33:E2:8A:44:45
Frank | A9:C2:82:72:99:B3
Harry
Sally
Frank
SWITCH
Broadcast

## Slide 10: A brief history (routy fruity)
And then, Frank’s entire family turned up so there were dozens or hundreds of devices on the network.
Lots of wasteful traffic broadcasting to the domain (NOISE)
So we segment the network into smaller chunks of multiple broadcast domains and add a ROUTER to control the segment
Broadcast only happens within it’s own broadcast domain
Routers use IP Addresses to identify hosts and groups of hosts as well as MAC Addresses
We add the IP addresses on each network segment to a ROUTING TABLE
The ROUTER directs traffic between segments using that lookup table. It is the GATEWAY to other networks.
The router only needs to know the next “hop” beyond itself and not the final destination
Sorted. All problems solved.
Harry
Sally
Francois
SWITCH
SWITCH
Router
10.0.110.0/24
192.168.110.0/24
Francesca
Frank
Frank Jr
Message
Header

## Slide 11: A brief history (net gain)
Routers allowed ever more complex topology.
And LO… The Internet was born.
NOTE: Not a series of tubes
Each router knows the best next HOP towards the destination but not the whole path
Harry
Sally
Frank
SWITCH
SWITCH
Message
Header

## Slide 12: Basic Routing
Router checks L2 header – makes sure this packet is for me
Checks L3 header to work out where to send the packet next
Uses RT to decide where to send the packet next
Replaces the L2 header with updated src and dst MAC info
 | My | Your
MAC | Got | ARP
IP | Got | DNS usually

## Slide 13: IP Addresses
IP Address is a 32 bit (4 byte) decimalisation of a binary address:
Written as four octets (8 bits each) with each number being between 0 and 255
      8.8.8.8
      00001000 00001000 00001000 00001000
Each address must be globally unique (usually)
Some address ranges are reserved for private use:
  10.0.0.0/8
  172.16.0.0/12
  192.168.0.0/16
Can’t use the same range on both sides of the router

## Slide 14: Subnetting (split the difference)
IP Addresses can be split into two parts
Network part indicates WHICH network a device is a member of
Host part indicates the unique number given to THAT device on the network
This “sub-net” allows us to route traffic to the group of hosts rather than know the final address of every device on every router in the path.
Subnet mask indicates which part of the IP address is the network part
Of the 32 bit address the mask number is the number of bits in the network
192.168.109.26/24
network
host
Subnet mask

## Slide 15: Subnetting (masking)
192.168.109.26 = 11000000 10101000 1101101 11010
We represent the subnet mask with binary
1 for network portion – 0 for host portion
11111111 11111111 11111111 00000000 (255.255.255.0)
Same as /24
192.168.109.26/24
network
host
Subnet mask
Network (24 bits)
host

## Slide 16: Subnetting (mask-tastic)
We can use masking to split subnets into smaller chunks for discrete groups of hosts and services
11111111 11111110 00000000 00000000 = /15 (255.254.0.0)
11111111 11111111 11111110 00000000 = /23 (255.255.254.0)
11111111 11111111 11111111 11111000 = /29 (255.255.255.248)
The smaller the subnet mask number the higher the number of hosts in that segment.
We refer to segments as “/24” etc as this is the number of “1” bits in the mask.

## Slide 17: DNS
Domain Name Service
Convert numeric IP addresses into alpha numeric names
Much more friendly
You can have private DNS (like AD)
You can have public DNS (like Cloudflare 1.1.1.1)
Used with DHCP (dynamic IP addressing) to allow multiple IPs for the same domain endpoint
It is hierarchical and split into “zones” that form a tree structure
You can “walk” the tree to reach your destination server

## Slide 18: DNS (zoning out)
The “.” zone is the root zone that holds the records for the top level domains like com. net. edu. (NOTE the trailing “.” that is usually ignored when displaying domain names)
e.g. uk1-dv.cloud.healthcare-uk.dxc.technology
“technology.” is the top level domain (tld) it holds a record pointing to “dxc.technology.” servers
“dxc.technology.” nameservers hold the pointer to “healthcare-uk.dxc.technology.”
“healthcare-uk.dxc.technology.” holds the pointer record to “cloud.healthcare-uk.dxc.technology.” which we hold in our Azure subscription and set to point at our environment load balancers.
We control everything under the “cloud” branch of the domain.
We are authoritative for that part of the domain

## Slide 19: That’s it
(sod off)